## Slide 1
Lead Safe Work Practices for the Non-Certified Renovation Worker
Adapted from the U.S. Environmental Protection Agency’s training for certified renovators and the New England Lead Coordinating Committee (NELCC: www.nelcc.uconn.edu)

## Slide 2: Who should take this course?
(1)
Work on renovation, repair, and painting jobs in homes, childcare facilities, and some schools built before 1978
(2)
Work under the direction of a
Lead-safe Certified Renovator
and
Take this course if you will

## Slide 3: Certified?
Non-certified?
This course is for
non-certified workers
It explains the skills you need to work lead-safe (under the direction of a Certified Renovator) but
It does not meet the training requirements to become a certified renovator.
Certified Renovator is a person who has been certified in lead-safe work practices by EPA or Kansas
Certified Renovators must take a different course than workers.

## Slide 4: Why should you take this course?
To meet the requirements of the EPA or Kansas if you work on homes, child-care facilities, and many schools built before 1978
To learn how to protect yourself, your family, your customers, and your community from lead poisoning

## Slide 5: Why 1978?
Structures built before 1978 may
contain lead paint
If you do not handle lead paint safely
You, the residents, their neighbors, your co-workers, and your own family can become lead poisoned
This training will teach you how to
work lead-safe

## Slide 6: What’s the connection between lead poisoning and renovation?
When renovation, repair, or painting jobs disturb lead paint, the paint often turns into lead dust
If people breathe or swallow lead dust, they can become lead poisoned
Lead poisoning can harm you, your family, your co-workers, the residents of the home, and their neighbors

## Slide 7: What harm does lead poisoning do?
Lead can cause serious, permanent problems with learning, behavior, and health
Lead can cause serious problems
with blood pressure, sexual function, digestion, and other illnesses
In young children
In adults

## Slide 8: By the end of this training, you will know how to
Setting up the job properly to keep dust and debris from spreading
Working so that you create as little dust as possible
Cleaning up completely
Prevent the spread of dangerous lead dust during renovation, repair, and painting work by

## Slide 9: You’ll work under the direction of a Certified Renovator
Perform lead-safe work as described in the EPA-RRP Rule and Kansas Department of Health and Environment (KDHE).
Train all non-certified workers in lead-safe
work practices.
Must be present to direct all non-certified workers during setup and cleanup.
Must be available by cell phone, and in Kansas, no more than 1 hour away from the work site
Maintain proof of their own certification and training records for all non-certified workers.
Certified Renovators

## Slide 10: Your responsibilities as a non-certified worker
Cooperate with the Certified Renovator in working lead-safe
Use the lead-safe work practices that you are being taught
Ask questions if you do not understand how to work lead-safe!
  A Certified Renovators must be available by cell phone at all times.
  A Certified Renovator must perform cleaning verification at the end of the job and maintain job records.

## Slide 11: EPA guidebook: Steps to Lead Safe Renovation, Repair and Painting
www.epa.gov/lead/pubs/steps.pdf

## Slide 12: 7 steps to lead-safe work
Certified Renovators must | Certified Renovators or non-certified worker must
1. Determine whether job involves lead paint | 
2. Be on site during set-up & final cleaning | 2. Set up safely
 | 3. Protect yourself
 | 4. Control the spread of dust
 | 5. Leave the work area clean
 | 6. Control waste
7. Verify cleaning or document clearance testing | 13

## Slide 13: Step 1
Does the job involve lead paint?
If you don’t work lead-safe
You, your family, or residents may become lead poisoned
If lead paint is present
You must use lead-safe
work practices
If you don’t know whether lead paint is present
You must assume that it
is present, AND
You must use lead-safe work practices
The main idea
Why?

## Slide 14: Step 1
Does the job involve lead paint?
Only these people can determine whether lead paint is present:
A Certified Renovator
(but not non-certified workers, including those who have taken this course)
A licensed lead inspector
A licensed lead risk assessor
How will you know?
A Certified Renovator
has been trained to
Use an EPA-approved lead test kit (Missouri only; not permitted in Kansas

## Slide 15: Step 1
Does the job involve lead paint?
How will you know?
If testing shows that no lead paint is present,
workers are not required to use lead-safe work practices

## Slide 16: Step 2
Set up safely:
Contain (isolate) work area
Keep out
People who are not
working on project
Pets that can track lead dust throughout the home
Keep in
Dust and debris
The main idea
Why?
To protect workers and residents
To prevent dust from spreading to rest of house
To make cleanup easier
at end of job

## Slide 17: Step 2
Set up safely:
Contain (isolate) work area
Signs
Barrier tape, rope, or fencing
Cones
Heavy-duty plastic sheeting
Masking, duct, or painter’s tape
Stapler
Utility knife or scissors
Supplies and tools you’ll need

## Slide 18: Step 2
Note: A Certified Renovator must be on-site while the work area is being set up.
Set up safely:
Keep people and pets out
How
Put up signs, tape, cones, fencing, or other barriers
Use signs in residents’ own
language
Ask owners to keep pets away from work area
Explain that keeping out of the work area protects
everyone from lead poisoning

## Slide 19: Step 2
Set up safely indoors: Keep dust and debris in
Take all moveable items out of work area
Cover items that cannot be moved with heavy plastic sheeting, and tape securely
Protect furniture and other belongings
Cover floors with heavy plastic sheeting at least 6 feet in all directions from work that will be done

## Slide 20: Step 2
Set up safely indoors: Keep dust and debris in
Close, cover with plastic sheeting, and seal
All windows
All doors (except for entry to work area)
All air vents
21
Seal off work area
If necessary, create airlock to enter and leave work area

## Slide 21: Step 2
22
Set up safely indoors
Put all tools and supplies on plastic sheeting before starting work

## Slide 22: Step 2
Set up safely outdoors: General
Cover ground and plants with heavy-duty plastic sheeting or tarps
  Extend sheeting/covering far enough to contain any dust and debris, minimum 10 feet in all directions
  Secure sheeting to building
Within 20 feet of work area
  Close and seal windows and doors
  Move or cover play areas
Put tools and supplies on protective sheeting before starting work
Keep dust and debris out of home

## Slide 23: Step 2
Set up safely outdoors: Vertical containment
Why? | To ensure that dust and debris do not contaminate nearby buildings or properties | 
When ? | When work affects surfaces within 10 feet of | 
 | property line | 
 | Wherever necessary to prevent contamination of Other buildings Other areas of the property Nearby buildings or properties | 
How? | Set up vertical containment or equivalent precautions | 

## Slide 24: Step 2
Set up safely outdoors: Special conditions
If working on 2nd story or above |  | Extend sheeting farther
If building is more than 3 stories high |  | Use vertical shrouding on scaffolding
If working close to sidewalk, street, or property boundary |  | Use vertical shrouding on scaffolding

## Slide 25: Step 2
Set up safely outdoors: Special conditions
If conditions are very windy
Avoid working in high winds if possible
If you must work, be very careful to keep dust and debris inside work area
You may need to make windscreen at edge of ground-cover plastic

## Slide 26: Step 2
Set up safely: Very dusty jobs
Turn off forced-air heating and air-conditioning systems
Set up vertical containment to limit size of work area
Examples
Opening up wall cavities
Removing old drop ceilings
Scraping paint
Dry sanding by hand
Usually require even more careful setup. All of the previous steps and

## Slide 27: Step 2
Set up safely: Maintain containment
Problems may occur after containment is set up Examples | What should you do? Fix them!
Tape comes loose | Put down more tape
Plastic sheeting gets torn | Repair or replace torn plastic sheeting
Paint chips fly off plastic during work | Extend plastic sheeting
 | Questions? Ask the Certified Renovator

## Slide 28: Step 3
Protect yourself
The main idea
Protect yourself from lead on the job |  | Avoid breathing and swallowing lead dust
Protect your family from lead poisoning |  | Avoid carrying lead dust home on your skin, hair, and work clothes

## Slide 29: Step 3
31
Protect yourself:
Personal Protective Equipment
Safety goggles or glasses
to protect your eyes
Disposable coveralls
to keep dust off your clothes
Disposable latex or rubber gloves to keep your hands clean,
especially when you eat

## Slide 30: Step 3
Protect yourself:
Personal Protective Equipment
Disposable shoe covers
to keep dust off your shoes and keep you from tracking dust out of the work area
Disposable painter’s hat
to keep dust out of your hair
Disposable N-100 respirator
to keep you from breathing lead dust

## Slide 31: Step 3
Protect yourself: At work
Wear personal protective equipment | 
Do not eat, drink, or smoke in work area | 
Wash your hands and face carefully | Each time you leave work area Before you eat or drink At end of each work day

## Slide 32: Step 3
Protect yourself and your family: After work
Clean your clothes
At end of work day, vacuum dust off clothes and shoes or put on clean clothes and shoes
  Use HEPA vacuum to collect dust
  Do not use compressed air to blow dust off clothing
Wash work clothes separately from household laundry
No hugging until you are clean
Do not hug anyone until you have
Changed out of your work clothes
Washed yourself thoroughly
34

## Slide 33: Step 4
Control the spread of dust
Create as little dust as possible
If you do create dust, keep it from spreading
The main idea

## Slide 34: Step 4
Control the spread of dust
Wet-dry sandpaper, sanding sponge
Misting bottle or pump sprayer
Heavy-duty plastic sheeting and bags
Utility knife or scissors
Masking, duct, or painter’s tape
Supplies and tools you’ll need
HEPA vacuum cleaner
Tack pads, paper towels, or
disposable wipes
For some jobs, you’ll also need
Low-temperature heat gun (heat guns not permitted in Kansas)
Chemical strippers without
methylene chloride
Power tools with HEPA attachments

## Slide 35: Step 4
Control the spread of dust
Mist areas before sanding, scraping, drilling, and cutting (except near live electrical outlets)
Score paint with utility knife before separating components
Pry and pull apart components instead of pounding and hammering
Create as little dust as possible
2
1
3

## Slide 36: Step 4
Control the spread of dust
Keep work area closed off from rest of home
Stay in contained work area and on contained paths
Don’t track dust and debris out of work area
  Remove disposable suit and shoe covers before you leave work area
  Clean shoes on tack pads or use damp paper towels to wipe off shoes before you step off protective sheeting
Keep dust within work area

## Slide 37: Step 4
Control the spread of dust
Before removing
  Wrap securely in heavy plastic sheeting or secure in heavy- duty plastic bags
  HEPA vacuum outside of bag
After removing
  Store in safe area
away from residents
To remove components from work area

## Slide 38: Step 4
Control the spread of dust: Prohibited practices
Do not use open-flame burning
Do not remove paint with high heat (heat guns must operate under 1,100 degrees Fahrenheit) (No heat guns in Kansas)
Do not use power tools, such as sanders and grinders, unless they are shrouded and have HEPA attachments
When working on lead paint

## Slide 39: Step 5
Leave work area clean
Leave work area completely clean of dust and debris
At end of every day
At end of job
Note: A Certified Renovator must be on-site while work area is being cleaned
Main idea

## Slide 40: Step 5
Leave work area completely clean of dust and debris
Heavy-duty plastic bags
Masking, duct, or painter’s tape
Misting bottle or pump sprayer
Disposable wet wipes or hand towels
HEPA vacuum with beater bar
Supplies and tools you’ll need

## Slide 41: Step 5
Leave work area completely clean of dust and debris
Detergent or general-
purpose cleaner
Mop and disposable mop heads
Two buckets or a two-
sided bucket with wringer
Shovel and rake
Wet mopping system
Swiffer®-type dry cloths
Supplies and tools you’ll need

## Slide 42: Step 5
Leave the work area clean: Every day
Clean and pick up as you work
  Vacuum work area with HEPA vacuum cleaner often
  Put trash in heavy- duty plastic bags
Wash your hands and face each time you leave work area
Throughout each day

## Slide 43: Step 5
Leave the work area clean: Every day
Clean entire work area and two feet beyond work area in all directions
Vacuum again with HEPA vacuum cleaner
Clean your tools
Wash well before you go home
Safely dispose of, or clean off, personal protective equipment
At end of each day

## Slide 44: Step 5
Leave the work area clean: At end of job
Keep sheeting that isolates work area in place until work area is completely clean
Remove plastic sheeting carefully
  Spray with water
  Fold with dirty side in
  Tape it shut
  Dispose of properly
Remove all dust, chips, trash, and debris, including building components, from work area
Vacuum all surfaces, including walls, with HEPA vacuum cleaner
  Use beater bar on carpets

## Slide 45: Step 5
Leave the work area clean: At end of job
Damp clean
Mist work area Scrub with general- purpose cleaner on wet rag or mop until all dust and debris are gone Change rinse water often
HEPA vacuum again
Let surfaces dry, and vacuum again
Inspect
Look around work area
  Also look 2 feet beyond work area and paths where debris was carried
  You should see no dust or debris
Clean area again thoroughly if you see any dust or debris

## Slide 46: Step 6
Collect and control waste
Contain waste at all times
On-site
When it is being removed from the site
The main idea

## Slide 47: Step 6
Collect and control waste: What is included?
Waste from painted surfaces
  Dust
  Debris
  Paint chips
  Architectural components
Protective sheeting
Dirty water
Cleaning supplies
  Mop heads
  Wipes
  HEPA filters
Protective gear
  Disposable clothing
  Gloves
  Respirators
Any other waste

## Slide 48: Step 6
Control waste: How to bag it
Bag and seal all waste before removing it from work area
Put all waste in heavy plastic sheeting or bags
Gooseneck seal bag with duct tape
  Double bag when necessary to prevent tears
Wrap large components in protective sheeting and seal with tape
HEPA vacuum outside of waste bags and bundles before removing them from the work area.

## Slide 49: Step 6
Control waste: How to store it
Store all waste in secure container or dumpster until disposal
Dispose of waste as soon as possible
Do not carry waste in open truck or personal vehicle

## Slide 50: Step 6
Control waste: Water
Check and follow federal, state, and local rules to dispose of water used to remove paint and to clean up
If rules allow, filter water and dump it in a toilet
If rules do not allow this method
  Collect water in a drum and remove from work site
  Do not dump water down a sink or tub, in a storm drain, or on the ground

## Slide 51: Step 6
Control waste: Disposal rules
EPA and KDHE consider most residential renovation, repair and painting activities “routine residential maintenance”.
Waste created by these activities
Is considered non-hazardous solid waste
Can be disposed of in an ordinary waste landfill
However, if your state or locality has stricter waste disposal requirements, you must follow the stricter rules.

## Slide 52: Step 7
Check the work: Visual inspection
Why? | To make sure no lead dust or debris is left behind
Who? | Certified Renovators only
How? | Looks carefully at entire work area If Certified Renovators sees dust, paint chips, or debris, clean again Repeat steps A and B until the Certified Renovator cannot see any dust, paint chips, or debris in work area

## Slide 53: Step 7
Check the work:
After passing visual inspection
Job is complete |  | Visual inspection must be followed by cleaning verification or clearance testing
For outside work
For all inside work

## Slide 54: Step 7
Cleaning verification or clearance testing?
Performed by contractor or landlord and
Not funded by federal government
Required for most • Required in projects that are
renovations that are
Performed by contractor or landlord and
Funded by federal government
May be requested by property owner instead of cleaning verification
54
5
Cleaning verification Clearance testing
Taking a dust wipe sample
Must be done by licensed lead inspector or risk assessor
Must be done by the Certified Renovators, not a worker

## Slide 55: Now you know the 7 steps to lead-safe renovation
7. Verify cleaning or document clearance testing
Determine whether the job involves lead paint
Set up safely
Protect yourself
Control the spread of dust
Leave the work area clean
Control the waste

## Slide 56: Check your learning
 | True | False
1. This course qualifies you to be a Lead-safe Renovator Supervisor. |  | 
2. Lead paint may be found in houses built before 1978. |  | 
3. Lead is dangerous for children but not for adults. |  | 
4. Common renovation activities can create dangerous lead dust. |  | 
5. Anyone can test to see whether a job involves lead paint. |  | 
6. People who are not working on a project should be kept out of the work area. |  | 
7. Keep windows in the work area open to provide fresh air. |  | 
8. It’s safe to drink but not to eat or smoke in the work area. |  | 
9. Regular power sanding is the best way to remove lead paint. |  | 
10. Use a HEPA vacuum for cleaning. |  | 

## Slide 57: Answer key
 | True | False
1. This course qualifies you to be a Lead Safe Renovation Supervisor. |  | X
2. Lead paint may be found in houses built before 1978. | X | 
3. Lead is dangerous for children but not for adults. |  | X
4. Common renovation activities can create dangerous lead dust. | X | 
5. Anyone can test to see whether a job involves lead paint. |  | X
6. People who are not working on a project should be kept out of the work area. | X | 
7. Keep windows in the work area open to provide fresh air. |  | X
8. It’s safe to drink but not to eat or smoke in the work area. |  | X
9. Regular power sanding is the best way to remove lead paint. |  | X
10. Use a HEPA vacuum for cleaning. | X | 

## Slide 58: Evaluation of this training
Was the information clear?
Do you still have questions about how to work lead-safe?

## Slide 59: Training record sheet
Non-certified worker’s name: Date: | Check below if worker viewed slides on the topic | Check below if worker completed hands-on activity
1. Determining whether job involves lead paint |  | Task must be done by certified LSRS
2. Setting up safely |  | 
Setting up barriers, signs, and flapped door entries |  | 
Covering or removing furniture |  | 
Controlling the spread of lead dust |  | 
Establishing containment indoors |  | 
Establishing containment outdoors |  | 
3. Using personal protective equipment |  | 
4. Cleaning up at the end of a job |  | 
Indoors |  | 
Outdoors |  | 
6. Bagging waste |  | 
7. Other: explain |  | 
7. Checking the work |  | Task must be done by certified LSRS
Inspecting visually |  | 
Cleaning verification |  | 
Signature of LSRS who conducted the training: |  |